## Slide 1: Senior Design Project: Color Filter
By Ezequiel Villanueva & Logan Doizaki
Notes: Introduce yourselves

## Slide 2: Presentation Outline
Project Description 3
Development 6
Architecture 8
Cost 18
Challenges 19
Demonstration + Q&A 21
Optimization 20
Notes: E

## Slide 3: Project Description
Notes: E

## Slide 4: Overview
A device was developed to take a colored image captured by a camera and apply color manipulation.
By using user-based inputs, specific colors are filtered. The modified image is displayed to the user and stored internally. Alongside this, a greyscale filter feature was created to show greyscale rather than showing a black image when all colors are filtered out.
Notes: L

## Slide 5: Examples
Color | Button 3 | Button 2 | Button 1 | Grayscale
RGB | LOW | LOW | LOW | LOW
RG | LOW | LOW | HIGH | LOW
RB | LOW | HIGH | LOW | LOW
RED | LOW | HIGH | HIGH | LOW
GB | HIGH | LOW | LOW | LOW
GREEN | HIGH | LOW | HIGH | LOW
BLUE | HIGH | HIGH | LOW | LOW
BLACK | HIGH | HIGH | HIGH | LOW
GRAY | X | X | X | HIGH
Notes: L

## Slide 6: Development
Notes: E

## Slide 7: OBJECTIVES FOR PROJECT
Setting up the microcontroller.
Color Filter
Grayscale
Finalizing Design
Notes: E

## Slide 8: Architecture
Notes: E

## Slide 9: Microcontroller
The Microcontroller serves to transmit and receive the image and user input information to their respective location.
Notes: E

## Slide 10: MCU (Circuit)
MCU for transmission and receiving data between all components
  Second MCU for more pin outputs
Using shifter registers to increase pin outputs by sending bit strings
Switches controlling what colors are filtered out
LCD screen for display
    Resolution is 128p X 128p
Notes: L

## Slide 11: MCU (CODE)
Takes JPEG image and converts to Bitmap
Extracts header and image data
Transmit Image Data and Filtering Information
Receives Filter Image Data
Reconstructs the Image in Parts with Multiplexers
Stores Images to SD Card which can be accessed on PC
Notes: E

## Slide 12: Color Filter
The Color filter utilizes logic masks to filter out specified colors
RGB information that consists of 24-bit color data per pixel.
Logic gates combined with masks
Notes: L

## Slide 13: Color Filter (Circuit)
The circuit is built with AND gates, Demultiplexers, and Multiplexers.
  The Demultiplexers are used to deconstruct 8-bit color data into its individual bits
  The AND gates are used to apply a mask to filter out the user selected colors.
  The Multiplexers is used for reconstruction of the signal.
Notes: E

## Slide 14: Color Filter (CODE)
The image taken by the MCU is broken into segments containing the file information and image data.
The image data is then transmitted to the color filter through a daisy chain of Shift Registers along with selector bit and mask information to indicate the bit position and filtering to be applied.
Once all three 8-bits are sent in parallel, the MCU reads the image provided by the Multiplexer and rebuilds the image 24 bits at a time.
Notes: L

## Slide 15: Grayscale
Greyscale is the representation of color using different shades of gray.
Greyscale is achieved by converting the 24-bits RGB data into 8-bit greyscale data
Since the amount of bits are reduced, there is some data loss.
Greyscale formula: Gray = (0.299 * Red) + (0.587 * Green) + (0.114 * Blue).
Notes: E

## Slide 16: GRAYSCALE (Circuit)
The circuit is built with Shifters, Full Adders, and a Multiplexer.
  The Shifters and Full Adders are used to perform the gray scale conversion.
    However, the conversion has a marginal error
      Gray = (0.25 * Red) + (0.5* Green) + (0.125 * Blue).
    This arithmetic is performed by doing bit division through the Shift Registers and addition through Full adders
  The Multiplexer is used to reconstruct the image
Notes: L

## Slide 17: GRAYSCALE (CODE)
The image taken by the MCU is broken into segments containing the file information and image data.
The image data is then transmitted to the color filter through a daisy chain of Shift Registers along with selector bit and mask information to indicate the bit position and filtering to be applied.
Once all three 8-bits are sent in parallel, the MCU reads the image provided by the Multiplexer and rebuilds the image 24 bits at a time.
Notes: E

## Slide 18
COST
Part | Cost
ESP32-S3-WROOM CAM Wireless Board | 26.04
Arduino Nano | 15.99
DSD TECH 1.8 Inch TFT LCD Display Module | 9.99
Switches/Buttons | 7.99
MicroSD | 14.99
De/Multiplexers | 10(0.65) = 6.50
Full Adders | 4(1.86) = 7.44
Shifters | 6(1.05) = 6.30
AND Gates | 36(0.42)= 15.12
Resistor Variety | 9.99
Prototype Board | 19.99
Solder Wire | 2(9.59) = 19.18
22 AWG Stranded Wire Spool Multicolor | 19.99
Tax(20%)+Shipping Estimate ($20) | 35.90+20
Total | $235.41
Notes: L/E

## Slide 19: Challenges ENCOUNTERED
Circuit
  PCB machine issues
    More time
  Running Out of Pins
    Shifters with bit strings
  Understanding Datasheets for Components
      Doing simulations of parts
    Multiplier is too expensive, hard to replicate
      Using shifters
    Shifters only shift to the left
      Inversing twice
    MUX
      Not possible to do the full reconstruction
  Faulty Soldering
  Circuit building program issues
    Finding components
    Making it look clean
Code
  Running out of Storage. MCU only has 512 KB
    External RAM provided by OPI PSRAM
  Misreading User Inputs
    Added Delay/Store data

## Slide 20: Optimization
  Reduce Processing Time:
    RGB: ~45.2 Seconds
    Gray: ~72.1 Seconds
  Future Project Ideas:
    Adding more controllability
      Amount of filtering
      Recoloring
    Live Feed Capability

## Slide 21: Q&A
Got Any Questions?
Demonstration + Q&A
Notes: Demonstration Here
- SD

## Slide 22: Thank You
Email us: evillan5@msudenver.edu
ldoizak1@msudenver.edu